## Slide 1: Washington Highway CMF Analysis
Benchmark vs Best Model MetaCount Research Group

## Slide 2: Objective
Show one thing clearly: does the new hierarchical model beat the benchmark model on out-of-sample performance, and what do the coefficient differences imply for safety interpretation.

## Slide 3: Dataset Snapshot
Metric | Value
Segments | 275
Response | FREQ (crash count)
Main exposure | AADT
Offset | log(Length)
Family used in selected model | NB2

## Slide 4: Benchmark Model
Baseline characteristics | Value
AADT treatment | Fixed offset style
AADT-varying CMFs | No
Random heterogeneity | No

## Slide 5: Best Model Found
Best-model characteristics | Value
AADT treatment | Estimated elasticity
AADT-varying CMFs | Yes
Random heterogeneity support | Yes (when RP refit available)

## Slide 6: Search Outcome (Concise)
Search convergence (selection-stage metrics).

## Slide 7
Search Phase | Candidates evaluated | Best BIC | Best Val RMSE | Median BIC | Median Val RMSE | First iter within 0.5% of best BIC
Simulated Annealing | 177.00 | 1,149.85 | 14.7784 | 1,174.27 | 17.2133 | 376.00
Harmony Search | 95.0000 | 1,155.37 | 13.7222 | 1,172.22 | 17.3585 | 131.00

## Slide 8: Benchmark vs Best: Key Result
Model | BIC | AIC | Test RMSE | Test Poisson Dev | Test R2
Benchmark (Ex16-3 literature model) | 1607.72 | 1577.18 | 14.186 | 315.17 | 0.5432
Hierarchical CMF (selected) | 1593.77 | 1556.44 | 12.8741 | 308.15 | 0.6238

## Slide 9
Lower BIC, lower Test RMSE, and higher Test R2 all point in the same direction: the best model outperforms the benchmark on held-out data.

## Slide 10: Observed vs Predicted Comparison
Observed and predicted crashes for benchmark vs best model.

## Slide 11: Difference Plot: Best Minus Benchmark
Prediction delta by traffic level: hierarchical minus benchmark.
Positive values mean the best model predicts more crashes than benchmark at that traffic level; negative values mean fewer.

## Slide 12: What Coefficient Differences Suggest About Safety
Parameter | Benchmark coef | Proposed coef | Safety implication
Intercept | -8.2280 | -7.0970 | higher value linked with lower crashes; weaker than benchmark
Average Longitudinal Slope (%) |  | -1.4595 | higher value linked with lower crashes; new or benchmark-missing term
log(AADT) |  | 0.883433 | higher value linked with higher crashes; new or benchmark-missing term
Average Longitudinal Slope (%) x log(AADT) |  | 0.149102 | higher value linked with higher crashes; new or benchmark-missing term
Lane Width (ft) |  | -0.093587 | higher value linked with lower crashes; new or benchmark-missing term
Minimum Vertical Grade (%) |  | -0.060196 | higher value linked with lower crashes; new or benchmark-missing term
Number of Horizontal Curves (count) |  | -0.022981 | higher value linked with lower crashes; new or benchmark-missing term
Posted Speed Limit (mph) |  | -0.011960 | higher value linked with lower crashes; new or benchmark-missing term

## Slide 13: Final Takeaway
Question | Answer
Did the best model beat benchmark on held-out data? | Yes
Is the improvement consistent across metrics? | Yes (BIC, RMSE, R2)
Does the model change safety interpretation? | Yes, via coefficient direction/magnitude differences and interaction effects

## Slide 14
Next action: use the safety-implication terms to prioritize policy checks on road segments where benchmark and best-model predictions diverge most.

## Slide 15: Appendix: Compact Coefficients
Parameter | Benchmark coef | Proposed fixed | Random mean | Random SD
Average Annual Precipitation (in/yr) x log(AADT) |  | 0.006028 |  | 
Average Longitudinal Slope (%) |  | -1.4595 |  | 
Average Longitudinal Slope (%) x log(AADT) |  | 0.149102 |  | 
Exposure Index | -0.066386 |  |  | 
Grade-Break Rate per Mile | 0.011867 |  |  | 
High-Snow Days per Year (snowfall > 1 in/day) | 0.212231 |  |  | 
Horizontal Curve Density (curves per mile) | 0.061300 |  |  | 
Intercept | -8.2280 | -7.0970 |  | 
Intersection Density (intersections per mile) | -0.027817 |  |  | 
Lane Width (ft) |  | -0.093587 |  | 
Lane Width (ft) x log(AADT) |  | 0.007206 |  | 
Low-Precipitation Days per Year (precip < 1.5 in/month) | -0.124630 |  |  | 
Minimum Vertical Grade (%) |  | -0.060196 |  | 
Number of Horizontal Curves (count) |  | -0.022981 |  | 
Pavement Friction, Skid Number (higher = more grip) | 0.015220 |  |  | 
Posted Speed Limit (mph) |  | -0.011960 |  | 
log(AADT) |  | 0.883433 |  |