## Slide 1: Washington Highway CMF Analysis
Hierarchical Crash Modification Factors MetaCount Research Group

## Slide 2: Data Overview
Metric | Value
Road segments | 275
Variables | 39
Response | Crash count (FREQ)
Traffic | AADT
Exposure | Length (log offset)
Model family | NB2
Category | Key Variables
Traffic | AADT, PEAKHR, ADTLANE, EXPOSE
Geometry | INCLANES, DECLANES, WIDTH, MEDWIDTH
Alignment | CURVES, MINRAD, TANGENT, GRADEBR
Grade | MIGRADE, MXGRADE, MXGRDIFF, SLOPE
Roadside | MIMEDSH, MXMEDSH, ACCESS, FRICTION
Climate | AVEPRE, AVESNOW, HISNOW, LOWPRE
Road class | URB, FC, SINGLE, DOUBLE, TRAIN
Auxiliary | INTPM, CPM, INTECHAG

## Slide 3: Methodology

## Slide 4
Upper terms — AADT-independent effect. CMF for a 1-unit change: . Same across all AADT levels.
Lower terms — modify the AADT elasticity:
CMF varies with traffic volume.
Search strategy
Random exploration: draw upper + lower variables from the candidate pool
Score on validation set by Poisson deviance and RMSE; reject non-monotonic AADT
Refinement stage: Simulated Annealing + Harmony Search
Final refit on train + validation (80%); evaluate on held-out test (20%)
Post-search random-parameters refit on the best spec
Hierarchical CMF model

## Slide 5: Search Convergence
Convergence: proposed-path trace (dotted) + running best solid envelope for BIC (left) and Validation RMSE (right). Green = monotonic AADT, grey = non-monotonic (excluded), star = global best.
Dotted line = all proposed models · Solid envelope = running best · Green = monotonic AADT · Grey = excluded · Star = global best
Metric scope note
Search-convergence plots report validation metrics during selection (train-fit evaluated on validation split).
Benchmark comparison slide reports held-out test metrics after final refit on train+validation.
These numbers are expected to differ because they are computed on different splits and at different fit stages.

## Slide 6: Refinement: Harmony Search & SA
Both refinement phases shown together: Harmony Search (left) and Simulated Annealing (right). BIC and Validation RMSE axes are windowed to show only competitive models. Running-best envelopes in bold; per-iteration proposals in lighter dots.
Bottom line: both refinement methods converged to the same winning specification.

## Slide 7
Phase | Best iteration | Best BIC | Best validation RMSE
Simulated Annealing | 2,203 | 1,147.82 | 16.2576
Harmony Search | 1,129 | 1,147.82 | 16.2576

## Slide 8: Simulated Annealing vs Harmony (Side-by-Side)
Best SA candidate vs best Harmony candidate by BIC and Validation RMSE.

## Slide 9: SA vs Harmony - Distribution Differences
Search Phase | Candidates evaluated | Best BIC | Best Val RMSE | Median BIC | Median Val RMSE | First iter within 0.5% of best BIC
Simulated Annealing | 42.0000 | 1,173.67 | 16.1397 | 1,184.19 | 17.8985 | 58.0000
Harmony Search | 23.0000 | 1,167.32 | 16.6192 | 1,177.42 | 17.3754 | 35.0000

## Slide 10: Final Model — Random-Parameters NB2
Full coefficient table: fixed effects + random parameters (Mean ± SD across sites)
Random parameters capture site-level heterogeneity in the effect of each variable.
Random-parameters summary
Type | Meaning
Fixed effects | Same coefficient for every segment
Random means | Average effect across sites
Random SDs | How much the effect varies by site

## Slide 11
Random-Parameters NB2 | unavailable
Compact random-parameter table unavailable in this run.

## Slide 12: Fixed-Effects Decomposition
Upper terms (AADT-independent CMFs) and lower terms (AADT-interaction effects)
Upper terms — direct CMF (same at any AADT level)
Variable | Full Name | Coefficient | CMF
Intercept | Intercept | -7.3088 | 
log(AADT) | log(AADT) Elasticity | +0.9113 | 
ACCESS | Access-Point Density (driveways + intersections per mile) | -0.1802 | 0.6436
AVESNOW | Average Annual Snowfall (in/yr) | +0.0473 | 1.0225
INTECHAG | Number of Grade-Change Points (count) | +0.1949 | 1.2536
MINRAD | Minimum Curve Radius (ft) - smaller = sharper bend | -0.0514 | 1.0000
MXGRADE | Maximum Vertical Grade (%) | +0.0685 | 1.0227
MXMEDSH | Maximum Median Shoulder Width (ft) | +0.1633 | 1.0688
SLOPE | Average Longitudinal Slope (%) | +0.1081 | 1.1425

## Slide 13
Lower terms — modify AADT elasticity
Variable | Full Name | Coefficient
CURVES | Number of Horizontal Curves (count) | -0.0153
WIDTH | Lane Width (ft) | -0.0207

## Slide 14: Benchmark Comparison
Hierarchical CMF vs Benchmark — key metrics
Model | BIC | AIC | Test RMSE | Test Poisson Dev | Test R2
Benchmark (Ex16-3 literature model) | 1607.72 | 1577.18 | 14.186 | 315.17 | 0.5432
Hierarchical CMF (selected) | 1597.91 | 1557.19 | 11.0846 | 268.28 | 0.7211

## Slide 15
What the numbers mean
Metric | Better is… | Result
BIC | Lower | Hierarchical wins
Test RMSE | Lower | Hierarchical wins
Test R² | Higher | Hierarchical wins
Lower BIC = model improvement is genuine, not overfitting
Lower RMSE = better predictions on unseen segments
Higher R² = more crash variance explained
Model difference
Feature | Benchmark | Hierarchical
AADT coefficient | Fixed = 1.0 | Estimated elasticity
Variable CMFs | Fixed only | Fixed + AADT-varying
Site heterogeneity | None | Random parameters
AADT monotonicity | Not enforced | Enforced during search

## Slide 16
Metric scope note
Search-convergence plots report validation metrics during selection (train-fit evaluated on validation split).
Benchmark comparison slide reports held-out test metrics after final refit on train+validation.
These numbers are expected to differ because they are computed on different splits and at different fit stages.

## Slide 17: Side-by-Side Model Forms
Form | Structure
Benchmark | log(mu_hat) = alpha + log(AADT) + log(L) + sum(beta_j * x_j)
Hierarchical | log(mu_hat) = alpha + beta_AADTlog(A) + sum(beta_jx_j) + sum(gamma_kx_klog(A)) + log(L)

## Slide 18
Main difference | Benchmark | Hierarchical
AADT slope | Fixed at 1.0 | Estimated
CMFs | Fixed only | Fixed + traffic-varying
Heterogeneity | None | Random parameters

## Slide 19: What Is Gained Beyond Benchmark CMFs
CMF capability: benchmark vs hierarchical approach
Capability | Benchmark SPF | Hierarchical CMF
Traffic-only CMF between two AADT levels | Yes: (A2/A1)^beta_AADT | Yes
Variable-specific CMF (lane width, shoulder, etc.) | No | Yes (upper terms)
AADT-varying CMF for a variable | No | Yes (lower terms)
Site heterogeneity in parameter effects | No | Yes (random parameters)
Monotonic AADT enforcement during selection | Not explicit | Explicit (elasticity constraint)

## Slide 20
Practical meaning: the benchmark can only scale crashes with traffic volume globally. The hierarchical model can answer policy questions like “how does widening shoulder or changing curvature affect risk at low vs high AADT, and how variable is that effect across sites?”
Benchmark CMF form: (A2/A1)^beta_AADT
Hierarchical CMF forms: exp(betadelta_x) and AADT^(gammadelta_x)

## Slide 21: Model Comparison — Baseline vs Hierarchical
Observed crashes + both predicted curves on the same AADT axes
Observed crashes (dots by split) vs polynomial-smooth predictions from the AADT-only benchmark (blue dashed) and the hierarchical CMF model (orange solid). Bottom panel shows normalised residuals for each model vs AADT.

## Slide 22
Model | BIC | AIC | Test RMSE | Test Poisson Dev | Test R2
Benchmark (Ex16-3 literature model) | 1607.72 | 1577.18 | 14.186 | 315.17 | 0.5432
Hierarchical CMF (selected) | 1597.91 | 1557.19 | 11.0846 | 268.28 | 0.7211

## Slide 23
Why curves can look similar: both models track the same traffic-exposure trend. The improvement appears in residual structure and test metrics (RMSE and R2), not only visual separation of smoothed lines.

## Slide 24: Prediction Delta vs AADT
Prediction difference by traffic level: hierarchical minus benchmark predicted crashes, plotted against log(AADT). Values above zero indicate the hierarchical model predicts more crashes; below zero indicates fewer than benchmark.

## Slide 25: AADT Response — Hierarchical Model
Observed vs hierarchical predictions with normalised residuals
Observed crashes vs hierarchical model polynomial smooth. Bottom: normalised residuals — orange = over-predicted, teal = under-predicted.

## Slide 26: The Fitted Model — Every Term Spelled Out
Upper terms — direct CMF (, same at any AADT)
Variable | Full Name | Coefficient | CMF
Intercept | Intercept | -7.3088 | 
log(AADT) | log(AADT) Elasticity | +0.9113 | 
ACCESS | Access-Point Density (driveways + intersections per mile) | -0.1802 | 0.6436
AVESNOW | Average Annual Snowfall (in/yr) | +0.0473 | 1.0225
INTECHAG | Number of Grade-Change Points (count) | +0.1949 | 1.2536
MINRAD | Minimum Curve Radius (ft) - smaller = sharper bend | -0.0514 | 1.0000
MXGRADE | Maximum Vertical Grade (%) | +0.0685 | 1.0227
MXMEDSH | Maximum Median Shoulder Width (ft) | +0.1633 | 1.0688
SLOPE | Average Longitudinal Slope (%) | +0.1081 | 1.1425

## Slide 27
Lower terms — modify AADT elasticity ()
Variable | Full Name | Coefficient
CURVES | Number of Horizontal Curves (count) | -0.0153
WIDTH | Lane Width (ft) | -0.0207

## Slide 28
Full equation:

## Slide 29: How to Read Each Coefficient as a CMF

## Slide 30
Upper term — fixed CMF at any AADT
A negative (e.g. shoulder width) means more of that variable = fewer crashes, at any AADT.
Lower term — CMF scales with traffic
A positive means the variable amplifies crash sensitivity to traffic. Higher-AADT roads feel this effect more strongly.
Quick reference
Sign | Term type | Effect
beta > 0 | upper | more = higher crash rate
beta < 0 | upper | more = lower crash rate
gamma > 0 | lower | amplifies AADT sensitivity
gamma < 0 | lower | dampens AADT sensitivity
Offset — log(Length)
Always included at coefficient = 1. A 2-mile segment is expected to have exactly twice as many crashes as a 1-mile segment with identical characteristics.
See “The Fitted Model” slide for every coefficient with exact values.

## Slide 31: Why More Trucks / Wider Median Can Mean More Crashes
Counter-intuitive results usually reflect correlated road types, not literal safety effects.
Variable | Sign | Likely interpretation
Double-unit trucks | Positive | Older rural corridors with heavier freight use
Median width | Positive upper term | High-speed divided arterials with more severe crashes

## Slide 32
Key insight: a large random-parameter SD means the effect varies strongly by site.

## Slide 33: Interactive CMF Dashboard
Interactive CMF Dashboard — open results/ex16_3_cmf/hierarchical_cmf_dashboard.html in any browser.
Feature | What it does
Variable dropdown | Select a model variable
Mode toggle | Switch between predicted crashes and CMF
AADT slider | Move between low and high traffic
Fan chart | Shows low / median / high response curves

## Slide 34
Fan chart key: parallel lines = upper-level effect · diverging lines = traffic-interaction effect

## Slide 35: Key Findings & Benefits
Benefit | Summary
Two-level structure | Separates baseline crash rate from traffic sensitivity
Random search | Optimises RMSE and Poisson deviance together
Monotonicity constraint | Keeps crashes increasing with traffic
Model result | Better BIC, lower RMSE, higher R² than the benchmark

## Slide 36
Run: python build_washington_presentation.py to regenerate HTML and PPTX.

## Slide 37: Appendix: Coefficients Side-by-Side
Benchmark vs proposed — all parameters
Parameter | Benchmark coef | Proposed fixed | Random mean | Random SD
Access-Point Density (driveways + intersections per mile) |  | -0.440641 |  | 
Average Annual Snowfall (in/yr) |  | 0.022268 |  | 
Average Longitudinal Slope (%) |  | 0.133219 |  | 
Exposure Index | -0.066386 |  |  | 
Grade-Break Rate per Mile | 0.011867 |  |  | 
High-Snow Days per Year (snowfall > 1 in/day) | 0.212231 |  |  | 
Horizontal Curve Density (curves per mile) | 0.061300 |  |  | 
Intercept | -8.2280 | -7.3088 |  | 
Intersection Density (intersections per mile) | -0.027817 |  |  | 
Lane Width (ft) x log(AADT) |  | -0.001281 |  | 
Low-Precipitation Days per Year (precip < 1.5 in/month) | -0.124630 |  |  | 
Maximum Median Shoulder Width (ft) |  | 0.066552 |  | 
Maximum Vertical Grade (%) |  | 0.022470 |  | 
Minimum Curve Radius (ft) - smaller = sharper bend |  | -0.000010 |  | 
Number of Grade-Change Points (count) |  | 0.225996 |  | 
Number of Horizontal Curves (count) x log(AADT) |  | -0.005089 |  | 
Pavement Friction, Skid Number (higher = more grip) | 0.015220 |  |  | 
log(AADT) |  | 0.911272 |  |